## Slide 1: Introduction to the Global Positioning System

## Slide 2: What is the GPS?
Orbiting navigational satellites
  Transmit position and time data
Handheld receivers calculate
  latitude
  longitude
  altitude
  velocity
Developed by Department of Defense

## Slide 3: History of the GPS
1969—Defense Navigation Satellite System (DNSS) formed
1973—NAVSTAR Global Positioning System developed
1978—first 4 satellites launched
Delta rocket launch

## Slide 4: History of the GPS
1993—24th satellite launched; initial operational capability
1995—full operational capability
May 2000—Military accuracy available to all users

## Slide 5: Components of the System
Space segment
24 satellite vehicles
Six orbital planes
  Inclined 55o with respect to equator
  Orbits separated by 60o
20,200 km elevation above Earth
Orbital period of 11 hr 55 min
Five to eight satellites visible from any point on Earth
Block I Satellite Vehicle

## Slide 6: The GPS Constellation

## Slide 7: GPS Satellite Vehicle
Four atomic clocks
Three nickel-cadmium batteries
Two solar panels
  Battery charging
  Power generation
  1136 watts
S band antenna—satellite control
12 element L band antenna—user communication
Block IIF satellite vehicle (fourth generation)

## Slide 8: GPS Satellite Vehicle
Weight
  2370 pounds
Height
  16.25 feet
Width
  38.025 feet including wing span
Design life—10 years
Block IIR satellite vehicle assembly at Lockheed Martin, Valley Forge, PA

## Slide 9: Components of the System
User segment
GPS antennas & receiver/processors
Position
Velocity
Precise timing
Used by
  Aircraft
  Ground vehicles
  Ships
  Individuals

## Slide 10: Components of the System
Ground control segment
Master control station
  Schreiver AFB, Colorado
Five monitor stations
Three ground antennas
Backup control system

## Slide 11: GPS Communication and Control

## Slide 12: GPS Ground Control Stations

## Slide 13: How does GPS work?
Satellite ranging
  Satellite locations
  Satellite to user distance
  Need four satellites to determine position
Distance measurement
  Radio signal traveling at speed of light
  Measure time from satellite to user
Low-tech simulation

## Slide 14: How does GPS work?
Pseudo-Random Code
Complex signal
Unique to each satellite
All satellites use same frequency
“Amplified” by information theory
Economical

## Slide 15: How does GPS work?
Distance to a satellite is determined by measuring how long a radio signal takes to reach us from that satellite.
To make the measurement we assume that both the satellite and our receiver are generating the same pseudo-random codes at exactly the same time.
By comparing how late the satellite's pseudo-random code appears compared to our receiver's code, we determine how long it took to reach us.
Multiply that travel time by the speed of light and you've got distance.
High-tech simulation

## Slide 16: How does GPS work?
Accurate timing is the key to measuring distance to satellites.
Satellites are accurate because they have four atomic clocks ($100,000 each) on board.
Receiver clocks don't have to be too accurate because an extra satellite range measurement can remove errors.

## Slide 17: How does GPS work?
To use the satellites as references for range measurements we need to know exactly where they are.
GPS satellites are so high up their orbits are very predictable.
All GPS receivers have an almanac programmed into their computers that tells them where in the sky each satellite is, moment by moment.
Minor variations in their orbits are measured by the Department of Defense.
The error information is sent to the satellites, to be transmitted along with the timing signals.

## Slide 18: GPS Position Determination

## Slide 19: System Performance
Standard Positioning System
  100 meters horizontal accuracy
  156 meters vertical accuracy
  Designed for civilian use
  No user fee or restrictions
Precise Positioning System
  22 meters horizontal accuracy
  27.7 meters vertical accuracy
  Designed for military use

## Slide 20: System Performance
Selective availability
Intentional degradation of signal
Controls availability of system’s full capabilities
Set to zero May 2000
Reasons
  Enhanced 911 service
  Car navigation
  Adoption of GPS time standard
  Recreation

## Slide 21: System Performance
The earth's ionosphere and atmosphere cause delays in the GPS signal that translate into position errors.
Some errors can be factored out using mathematics and modeling.
The configuration of the satellites in the sky can magnify other errors.
Differential GPS can reduce errors.

## Slide 22: Application of GPS Technology
Location - determining a basic position
Navigation - getting from one location to another
Tracking - monitoring the movement of people and things
Mapping - creating maps of the world
Timing - bringing precise timing to the world

## Slide 23: Application of GPS Technology
Private and recreation
  Traveling by car
  Hiking, climbing, biking
  Vehicle control
Mapping, survey, geology
English Channel Tunnel
Agriculture
Aviation
  General and commercial
  Spacecraft
Maritime

## Slide 24: GPS Navigation

## Slide 25: GPS News
http://www.gpseducationresource.com/gpsnews.htm
One–page reading exercise
  Center of page—main topic
  Four corners—questions & answers from reading
  Four sides—specific facts from reading
  Spaces between—supporting ideas, diagrams, definitions
  Article citation on back of page

## Slide 26: Military Uses for the GPS
Operation Desert Storm
Featureless terrain
Initial purchase of 1000 portable commercial receivers
More than 9000 receivers in use by end of the conflict
Foot soldiers
Vehicles
Aircraft
Marine vessels

## Slide 27: Geocaching
Cache of goodies established by individuals
Coordinates published on Web
Find cache
  Leave a message
  Leave some treasure
  Take some treasure
http://www.geocaching.com/

## Slide 28: Handheld GPS Receivers
Garmin eTrex
  ~$100
Garmin-12
  ~$150
Casio GPS wristwatch
  ~$300
The GPS Store

## Slide 29: GPS Operation Jargon
“Waypoint” or “Landmark”
“Track” or “Heading”
“Bearing”
CDI
Route
Mark
GOTO
    GPS/Digital Telephone

## Slide 30: GPS Websites
USNO NAVSTAR Homepage
  Info on the GPS constellation
How Stuff Works GPS
  Good everyday language explanation
Trimble GPS tutorial
  Flash animations
GPS Waypoint registry
  Database of coordinates

## Slide 31: Classroom Applications
Physics
  Distance, velocity, time
  Orbital concepts
Earth Science
  Mapping
  Spacecraft
Environmental Science
  Migratory patterns
  Population distributions
  GLOBE Program
Mathematics
Geography
Technology

## Slide 32: Classroom Applications
Careers
Aerospace
  Satellite vehicles
  Launch vehicles
Hardware engineering
  Ground control systems
  User systems
Software engineering
Research careers

## Slide 33: In and Out of the Classroom

## Slide 34: Problem Solving

## Slide 35: Sometimes the solution is over your head . . .